## Slide 1: Lecture 1
Data formats, reading, plotting
Lecture notes and examples:
https://github.com/irfu/Nordita_Magnetic_Reconnection_School_2015

## Slide 2: Software setup
Requirements:
  Matlab 2013b+ (older versions might work)
  git or github
  CSA (Cluster Science Archive) account
IRFU-matlab at GitHub:
  https://github.com/irfu/irfu-matlab
  To fetch to you computer use:
  git clone https://github.com/irfu/irfu-matlab.git
  Creates a sub-directory “irfu-matlab” which needs to be added to your path, e.g.:
  >> addpath /Users/yuri/devel/irfu-matlab

## Slide 3: Test that everything works
>> addpath('/Users/yuri/devel/irfu-matlab/')
>> irf
Added to path: /Users/yuri/devel/irfu-matlab/contrib/isdat
Added to path: /Users/yuri/devel/irfu-matlab/contrib/libirbem
Added to path: /Users/yuri/devel/irfu-matlab/contrib/libcef
Added to path: /Users/yuri/devel/irfu-matlab/contrib/matlab_central
Added to path: /Users/yuri/devel/irfu-matlab/contrib/matlab_central/cm_and_cb_utilities
Added to path: /Users/yuri/devel/irfu-matlab/contrib/mice
Added to path: /Users/yuri/devel/irfu-matlab/contrib/nasa_cdf_patch
Added to path: /Users/yuri/devel/irfu-matlab/irf
Added to path: /Users/yuri/devel/irfu-matlab/plots
Added to path: /Users/yuri/devel/irfu-matlab/mission/cluster
Added to path: /Users/yuri/devel/irfu-matlab/mission/cluster/caa
Added to path: /Users/yuri/devel/irfu-matlab/mission/solar_orbiter
Added to path: /Users/yuri/devel/irfu-matlab/mission/themis
Added to path: /Users/yuri/devel/irfu-matlab/mission/mms
Added to path: /Users/yuri/devel/irfu-matlab/mission/mms/mms_testFunctions
irfu-matlab version: v1.9.3
Checking if you have latest irfu-matlab... YES:)
Reading file /Users/yuri/devel/irfu-matlab/contrib/libcef/C1_CP_EFW_L3_P__20010201_120000_20010201_120100_V110503.cef.gz, please wait...
8 variables and 15 records read
CEFLIB is OK
loading datastore...
SPICE/MICE is OK
IRBEM is OK
CDF_LEAPSECONDSTABLE was not set in user environment.
Automatically setting it to: /Users/yuri/devel/irfu-matlab/contrib/nasa_cdf_patch/CDFLeapSeconds.txt
Operating system is OK
>>

## Slide 4: Data formats
CEF – Cluster Exchange Format
  Base format for ESA CSA
  Text based, nicely standardized metadata: http://caa.estec.esa.int/caa/documentation.xml
  Self-contained: metadata header and data in the same file
CDF – NASA Common Data format
  Binary format
  Used for MMS, THEMIS, Cluster (using CEF->CDF converter), and many other missions
  ISTP convention for metadata
  Self-contained: Global and Variable attributes, data in the same file

## Slide 5: Exercise 1
Objective: Download CDF files from CSA and examine file contents
Matlab code:
>> tint = '2002-03-30T13:11:30Z/2002-03-30T13:12:00Z';
>> caa_download(tint,'C?_CP_FGM_FULL');
Prompt for CSA username & password
>> ls
CAA
>> ls CAA
C1_CP_FGM_FULL C2_CP_FGM_FULL C3_CP_FGM_FULL C4_CP_FGM_FULL
>> ls CAA/C1_CP_FGM_FULL/
C1_CP_FGM_FULL__20020330_131130_20020330_131200_V140306.cdf

## Slide 6: Ex 1: cont
>> info=spdfcdfinfo('CAA/C1_CP_FGM_FULL/C1_CP_FGM_FULL__20020330_131130_20020330_131200_V140306.cdf')
info =
Filename: 'C1_CP_FGM_FULL__20020330_131130_20020330_131200_V140306.cdf'
FileModDate: '25-Jul-2015 23:25:41'
FileSize: 137987
Format: 'CDF'
FormatVersion: '3.3.1'
FileSettings: [1x1 struct]
Subfiles: {}
Variables: {11x9 cell}
GlobalAttributes: [1x1 struct]
VariableAttributes: [1x1 struct]
LibVersion: '3.6.0'
PatchVersion: '3.6.0.4'

## Slide 7
>> info.GlobalAttributes
ans =
LOGICAL_FILE_ID: {'C1_CP_FGM_FULL__20020330_131130_20020330_131200_...'}
VERSION_NUMBER: {'140306'}
DATASET_VERSION: {3x1 cell}
FILE_TIME_SPAN: {'30-Mar-2002 13:11:30.000 30-Mar-2002 13:12:00.000'}
GENERATION_DATE: {'25-Jul-2015 21:25:40.000'}
FILE_CAVEATS: {4x1 cell}
MISSION: {'Cluster'}
MISSION_TIME_SPAN: {'16-Aug-2000 12:39:00.000 31-Dec-2030 23:59:59.000'}
MISSION_AGENCY: {'ESA'}
MISSION_DESCRIPTION: {5x1 cell}
MISSION_KEY_PERSONNEL: {'Philippe Escoubet>Philippe.Escoubet@esa.int >Clu...'}
MISSION_REFERENCES: {'The Cluster and Phoenix Missions>Cluster project...'}
MISSION_REGION: {11x1 cell}
MISSION_CAVEATS: {'*CL'}
OBSERVATORY: {'Cluster-1'}
OBSERVATORY_CAVEATS: {'*C1_CQ'}
OBSERVATORY_DESCRIPTION: {8x1 cell}
OBSERVATORY_TIME_SPAN: {'16-Jul-2000 12:39:00.000 31-Dec-2030 23:59:59.000'}
OBSERVATORY_REGION: {11x1 cell}
EXPERIMENT: {'FGM'}
EXPERIMENT_DESCRIPTION: {13x1 cell}
INVESTIGATOR_COORDINATES: {'Chris Carr>PI>c.m.carr@imperial.ac.uk'}
EXPERIMENT_REFERENCES: {3x1 cell}
EXPERIMENT_KEY_PERSONNEL: {'Chris Carr>PI>c.m.carr@imperial.ac.uk'}
EXPERIMENT_CAVEATS: {'*CL_CQ_FGM_CAVF.txt'}
INSTRUMENT_NAME: {'FGM1'}
INSTRUMENT_DESCRIPTION: {'FGM Experiment on Cluster C1'}
INSTRUMENT_TYPE: {'Flux_Feedback'}
MEASUREMENT_TYPE: {'Magnetic_Field'}
INSTRUMENT_CAVEATS: {'*C1_CQ_FGM_CAVF'}
DATASET_ID: {'C1_CP_FGM_FULL'}
DATA_TYPE: {'CP>CAA Parameter'}
DATASET_TITLE: {'Magnetic field, full resolution'}
DATASET_DESCRIPTION: {2x1 cell}
CONTACT_COORDINATES: {'Chris Carr>PI>c.m.carr@imperial.ac.uk'}
TIME_RESOLUTION: {'0.04461'}
MIN_TIME_RESOLUTION: {'0.04461'}
MAX_TIME_RESOLUTION: {'0.01487'}
PROCESSING_LEVEL: {'Calibrated'}
ACKNOWLEDGEMENT: {'Please acknowledge the FGM team and ESA Cluster ...'}
DATASET_CAVEATS: {'*C1_CQ_FGM_CAVF'}
FILE_TYPE: {'cef'}
METADATA_TYPE: {'CAA'}
METADATA_VERSION: {'2.0'}
Software_version: {'QIE V_3.6.2 [Feb 2012]'}

## Slide 8
>> info.Variables
ans =
Columns 1 through 6
'time_tags__C1_CP...' [1x2 double] [2018] 'epoch' 'T/' 'Full'
'half_interval__C...' [1x2 double] [2018] 'single' 'T/' 'Full'
'B_vec_xyz_gse__C...' [1x2 double] [2018] 'single' 'T/T' 'Full'
'B_mag__C1_CP_FGM...' [1x2 double] [2018] 'single' 'T/' 'Full'
'sc_pos_xyz_gse__...' [1x2 double] [2018] 'single' 'T/T' 'Full'
'range__C1_CP_FGM...' [1x2 double] [2018] 'int32' 'T/' 'Full'
'tm__C1_CP_FGM_FULL' [1x2 double] [2018] 'int32' 'T/' 'Full'
'B_vec_xyz_gse__C...' [1x2 double] [ 1] 'char' 'F/T' 'Full'
'B_vec_xyz_gse__C...' [1x2 double] [ 1] 'char' 'F/T' 'Full'
'sc_pos_xyz_gse__...' [1x2 double] [ 1] 'char' 'F/T' 'Full'
'sc_pos_xyz_gse__...' [1x2 double] [ 1] 'char' 'F/T' 'Full'
Columns 7 through 9
'None' [2018] []
'None' [2018] []
'None' [2018] []
'None' [2018] []
'None' [2018] []
'None' [2018] []
'None' [2018] []
'None' [ 1] []
'None' [ 1] []
'None' [ 1] []
'None' [ 1] []
>>

## Slide 9: Time